SSA MICROCODE
                                                      INSTALLATION INSTRUCTIONS

                                                               INSTALL SSAFLASH
                                               MICROCODE FOR SSA 4-PORT ADAPTER
                                                              FEATURE CODE 6214
                                      MICROCODE FOR ENHANCED SSA 4-PORT ADAPTER
                                                              FEATURE CODE 6216
                                                 MICROCODE FOR SSA RAID ADAPTER
                                                         FEATURE CODE 6217/6218
                                              MICROCODE FOR SSA DISKS DFHC/DCHC



                                                                 FIELD USE ONLY








                                                                    SEP 11,1997





                                                                    SSD 7133 PE
                                                                 MP26/19 Havant
                                                          external 01705-486363
                                                            internal (7)-215732
                                                             NWARWICK at WINVMD

                                             Written By:   D Sinclair/N Warwick
                                             Approved By:  EC Management Team


  1.0  USING THE NEW  ADAPTER AND DRIVE MICROCODE DISKETTES
  ___________________________________________________________________

  This document describes how to install the new microcode for the SSA Adaptors
  and SSA Dasd.  The microcode is supplied on two diskettes:

  o   Adapter microcode diskette containing file adap2137.BFFBIN
  o   Disk Drive microcode diskette containing file DISK8381.BFFBIN
  o   Disk Drive microcode diskette containing file 6561.BFFBIN


  2.0 INSTALLING THE ADAPTER MICROCODE

  The SSA Adapter Microcode diskette contains the latest level of microcode
  code for the SSA 4-Port Adapter, feature number 6214, the Enhanced SSA
  4 Port Adapter, feature number 6216, the SSA Raid Adaptor, feature
  number 6217 and 6218.

  To load the microcode:

  1.  Log in as root

  2.  Insert the adap2137.bff Adaptor Microcode diskette in the drive rfd0

  3.  Enter the command: "installp -ac all"

  4.  Run cfgmgr to download the adaptor microcode to every adaptor
      installed in the system.

  5.  If the adapter is on an SSA loop that includes an adapter in another
      system, you must update the  adapter  microcode in that other
      system. See  2.1, "Installing the Adapter Microcode into Adapters in
      Other Systems."


  2.1 INSTALLING THE ADAPTER MICROCODE INTO ADAPTERS IN OTHER SYSTEMS

  It is recommended that on an SSA loop, all SSA adapters of a particular type
  use a common level of microcode.  If the adapters are all in one system,
  they automatically receive a common level of microcode.    If the adapters
  are in different systems, you should update the adapter microcode in
  those systems as soon as is possible.

  Where appropriate:

  1.  Log in as root.

  2.  Insert the SSA Adapter Microcode diskette into the drive rfd0.

  3.  Enter the command: "installp -ac all"

  4.  Run cfgmgr to download the adaptor microcode to every adaptor
      installed in the system.

  5.  ATTENTION:  In this step, do not run Advanced Diagnostics.

      On each system that is connected to a particular SSA loop, go into System
      Verification mode, and run diagnostics to ensure that  all  the  adapters
      are  in  a valid loop.   (For example, a loop that contains an SSA 4-Port
      Adapter can include only one other adapter.)


  3.0    INSTALLING THE DISK8381.bff DISK DRIVE MICROCODE
  ______________________________________________________

  This SSA Disk Drive Microcode diskette contains the latest level of
  microcode (8372 and 8181) for SSA Disk Drives.
  This level of code must be installed
  on all AIX 4.1.5/4.2.1 systems containing the SSA 4 Port Raid Adaptor.
  NOTE This code can only be downloaded with the service aids if the
  4.1.5. or 4.2.1. SSA device drivers are installed.

  3.1  Downloading the Microcode to the etc/microcode Directory of the
                       Specific Machine:
   ______________________________________________________

  1.  Insert the DISK8381.bff Disk Drive Microcode diskette
      in the drive rfd0

  2.  Log in as root

  3.  Enter the command: "installp -ac all"

 3.2  Downloading the Microcode from the etc/microcode Directory of the
               Specific Machine to the SSA DASD
  ______________________________________________________

  The following steps should be followed for all systems in the loop:

  1.
  a/ Stop all io activity on the SSA drives you are loading uCode to.
  b/ Unmount all filesystems on the SSA drives you are loading uCode to.
  c/ varyoff all volume groups on the associated SSA drives

  2.  Run the following command to load the latest available
      microcode to all drives that require it.

NOTE  If there are other systems in the same SSA loop then ONLY perform
      this step on one system in the loop.DO NOT perform it concurrently
      on multiple systems in the loop.

      ssadload -u


    3.3 INSTALLING THE DISK DRIVE MICROCODE INTO DISKS IN OTHER SYSTEMS
    ______________________________________________________

  Once a disk has been downloaded from one system, it is not necessary
  to download the same code from other systems on the same SSA loop.
  However, it is sensible to install the latest disk drive code onto
  all hosts.  Where appropriate:

  1.  Log in as root

  2.  Insert the DISK8381.bff  Disk Drive Microcode diskette
      in the drive rfd0.

  3.  Enter the command: "installp -ac all"

  3.4  INSTALLING THE 6561.bff DISK DRIVE MICROCODE
  ___________________________________________________

  This microcode diskette provides the 6561 level of code for
  DFHC type SSA disk drives.  If you are able to install the
  DISK8381.bff SSA disk microcode as described in 3.1.1 you
  can omit installation of the 6561.bff SSA disk microcode, since the
  DISK8381.bff SSA disk microcode supercedes the 6561.bff SSA
  disk microcode.

  To load the microcode:


  1.  Insert the 6561.bff Disk Drive Microcode diskette in the drive rfd0

  2.  Log in as root

  3.  the following steps should be followed for all systems in the loop:

  a/ Stop all io activity on the SSA drives you are loading uCode to.
  b/ Unmount all filesystems on the SSA drives you are loading uCode to.
  c/ varyoff all volume groups on the associated SSA drives

  4.  Enter the command: "installp -ac all"

  5.  When you have finished installing all the microcode (adapter and disk)
      then reboot or run "cfgmgr" for the changes to take effect.
      If there are other systems in the same loop perform the following :

 3.5 INSTALLING THE DISK DRIVE MICROCODE INTO DISKS IN OTHER SYSTEMS
  ___________________________________________________________________

  Once a disk has been downloaded from one system, it is not necessary
  to download the same code from other systems on the same SSA loop.
  However, it is sensible to install the latest disk drive code onto
  all hosts.  Where appropriate on each system:

    5.1.  Log in as root

    5.2.  Insert the 6561.bff Disk Drive Microcode diskette in the
          drive rfd0

    5.3.  Enter the command: "installp -ac all"


 3.6 ACTIONS TO BE TAKEN WHEN NEW DISKS ARE ADDED TO THE SYSTEM
  ________________________________________________________________

  Since the disk download mechanism used for disk8381.bff is a manual
  process it is necessary to repeat from step (2) in 3.2 whenever new
  disks are added to a particular system.  This ensures all
  attached disks are kept at the latest level of code.

  Disk drive code installed from 6561.bff is installed automatically
  on SSA disks where required at boot time.